## Slide 1: MATLAB and Simulink for Control Systems
Dr. P. Sumathi
Assistant Professor
DA-IICT, Gandhinagar

## Slide 2: Contents
Introduction to MATLAB and Simulink
Control system toolbox
Creating control system models
Time and frequency response analysis
P, PI, PD, PID controllers
Discrete time systems

## Slide 3: MATLAB
Language of Technical computing
High level language and interactive environment
Maintained by The Mathworks, Inc. of Natick, Massachusetts.
Available for MS windows and other computer systems.
The language was developed in the 1970s for applications involving matrices, linear algebra and numerical analysis.
MATLAB stands for “Matrix Laboratory”
It has a number of add-on software modules, called toolboxes which performs more specialized computations.

## Slide 4: Simulink
Simulation and Model-Based design
Integrated with MATLAB
Environment for multidomain simulation and Model-Based design for dynamic and embedded systems
Provides interactive graphical environment
Contains Block libraries  design, test and implement a variety of systems
Add-on Products  A number of Mathworks and third party hardware and software products

## Slide 5: Starting MATLAB
Double click on the MATLAB Icon
You will see the MATLAB Desktop – command window and Help browser
Default Desktop layout:
Command Window – Communicate with the MATLAB program
Command History – Shows the previous keystrokes entered in the command window
Current Directory – Path of the working directory
Workspace – Displays the variables in the current workspace
MATLAB displays the prompt (>>) to indicate that it is ready to receive instructions.
Cursor should be placed just after the prompt.

## Slide 6: Starting MATLAB - MATLAB Desktop
Workspace
Command Window
Command History
Current Directory
Tool Bar

## Slide 7
Entering Commands and Expressions
Matrix Operations
Plotting with MATLAB
Creating m file

## Slide 8: Control System Toolbox
Creating linear models.
tf - Create transfer function (TF) models.
zpk - Create zero/pole/gain (ZPK) models.
ss - Create state-space (SS) models.
Conversions.
c2d - Continuous to discrete conversion.
d2c - Discrete to continuous conversion.
d2d - Resample discrete-time model.
tf2ss, ss2tf - one model to another

## Slide 9
Time-domain analysis.
step - Step response.
stepinfo - Step response characteristics (rise time, ...)
impulse - Impulse response.
initial - Free response with initial conditions.
lsim - Response to user-defined input signal.
Compensator design.
rlocus - Evans root locus.

## Slide 10
Frequency-domain analysis.
bode - Bode diagrams of the frequency response.
lti/bodemag - Bode magnitude diagram only.
margin - Gain and phase margins.
nyquist - Nyquist plot.
nichols - Nichols plot.
lti/allmargin - All crossover frequencies and related gain/phase margins.
lti/freqresp - Frequency response over a frequency grid.
lti/evalfr - Evaluate frequency response at given frequency.
Graphical User Interfaces.
ltiview - LTI Viewer (time and frequency response analysis).

## Slide 11
System interconnections.
append - Group LTI models by appending inputs and outputs.
parallel - Connect LTI models in parallel (overloaded +).
series - Connect LTI models in series (overloaded *).
feedback - Connect LTI models with a feedback loop.
lti/connect - Arbitrary interconnection of LTI models.
sumblk - Specify summing junction (for use with CONNECT).
Overloaded arithmetic operations.
+ and - - Add and subtract systems (parallel connection).
* - Multiply systems (series connection).
\ - Left divide -- sys1\sys2 means inv(sys1)*sys2.
/ - Right divide -- sys1/sys2 means sys1*inv(sys2).
^ - Powers of a given system.
' - Pertransposition.
.' - Transposition of input/output map.
.* - Element-by-element multiplication.
[..] - Concatenate models along inputs or outputs.

## Slide 12
State-space (SS) models.
canon - State-space canonical forms.
ctrb - Controllability matrix.
obsv - Observability matrix.

## Slide 13: Simulink
Simulink Library Browser
Model file

## Slide 14: Simulink models
Time Response
Mux
Mux

## Slide 15: Simulink models

## Slide 16: State space model

## Slide 17: Compensated System

## Slide 18: Simulink models

## Slide 19: PID Controller

## Slide 20: Discrete Time systems

## Slide 21: AM Modulation

## Slide 22: AM Modulation

## Slide 23
Thank you